## Slide 1
What’s Happened to Our
Nuclear Waste Disposal Program?
Dr. James Conca and Dr. Judith Wright TCLBA
Parker Foundation/UFA Ventures, Inc./Los Alamos/WSUTC Richland, WA
Richland, WA http://www.forbes.com/sites/jamesconca/ February 2019

## Slide 2
Spent Nuclear Fuel (SNF)
High Level Waste (HLW)
Transuranic Waste (TRU-CH&RH)
Low Level Waste (LLW)
Radioactivity
Dose Rate
RH
CH
Contact Handled (CH) < 200 mrem/hr < Remote Handled (RH)
Categories of Nuclear Waste In the U.S.
Deep Geologic Disposal is required for SNF, HLW and TRU
WA State has all four types of nuclear waste, especially TRU and HLW

## Slide 3
a short nuclear primer
235U - splits (fissions) easily
238U - does not fission easily
Natural uranium (ore) is 0.7% 235U and 99.3% 238U
Nuclear fuel is enriched to ~4% 235U, with ~96% 238U
Nuclear weapons must be enriched to >93.5% 235U
Yellowcake
U3O8
Uranium-ore
Notes: So what about the waste?

## Slide 4
proton
neutron
92 protons
+ 143 neutrons
235 total
Fission of 235U
235U
Resultant formation of two unequal pieces (fission products), 3 neutrons and a small amount of mass turned into energy
90Sr
137Cs
235U
235U
235U

## Slide 5
proton
neutron
Neutron Capture by 238U  239Pu

U
92
238
U
92
239

Np
93
239
Pu
94
239
90Sr
137Cs
formation of the actinides
In fuel most of what these
released neutrons hit is 238U

## Slide 6
URANIUM
DISSOLUTION
URANIUM
SEPARATION
COATING REMOVAL WASTE
Other SSTs
SSTs B-201 through B-204,
T-201 through T-204,
and T-104, T-110, & T-111
REPROCESSING
BUILDING 224 CONCENTRATION WASTES
PLUTONIUM DECONTAMINATION
1ST DECON
CYCLE
2ND DECON
CYCLE
IN 224 B & T
PROCESSING PLANTS
PLUTONIUM
CONCENTRATION
PLUTONIUM PRODUCT
METAL WASTE
HLW
TRU
DECONTAMINATION CYCLE
WASTES
FUEL
ASSEMBLIES
CLADDING REMOVAL
(Coating Dissolution)
HLW & TRU are both nuclear bomb waste
- SNF is not
Since 1970, most Cs/Sr has been removed, others mostly decayed, so now most tanks are TRU or LLW
- 57 million gallons at Hanford
- most is now TRU or LLW
~ 600k gallons are HLW
IRRADIATED FUEL

## Slide 7
What are the costs of over-regulating nuclear?
$7 million is the value of a human life according to EPA
$316,000 is the average paid out in health care over a life
$129,000 is the average historic legal value of a human life
$45 million (value of a single healthy human life when chopped up and sold on the black market for body parts)
$12,420 (death benefit to families of deceased soldiers)
$2.5 billion per theoretical human life saved (LNT vs 0.1 Sv/yr)
$100 per human life saved by immunization against measles, diphtheria, and pertussis in developing countries
How Much Do We Consider the Value of a Human Life to be?

## Slide 8: Three Ways Science Enters The Decision-Making Process
(1) Does not enter at all --➣ Ignored
(2) Enters before decision is made --➣ Science-Based Decision
(3) Enters after decision is made --➣ Science-Supported Decision
Our nuclear waste program started out as (2) but then became (3)

## Slide 9: National Academy of Sciences (NAS) concludes in 1957 that the most promising disposal option for all radioactive waste is in massive salt deposits
1957
“Salt at great depth ‘flows.’ It will encapsulate any waste placed at depth and isolate it from the surface environment for eons.” - NAS
“The great advantage is that no water can pass through salt. Fractures are self healing..” – NAS
It takes a billion years for water to move an inch in this rock

## Slide 10: 1957 - deep geologic disposal adopted; salt chosen as best 1970 - AEC establishes new category for transuranic waste, distinct from low- and high-level radioactive waste but with significant overlap in radioactivity. EPA formed. 1976 – reprocessing of commercial spent fuel put on hold; retrievable disposal concept born for SNF/HLW; salt is out; separate HLW disposal site is sought. TRU still to go into salt. 1982 – Nuclear Waste Policy Act…
Radioactivity
Dose Rate
Volume
Radioactivity
RH
CH
RH
CH
Contact Handled (CH) < 200 mrem/hr < Remote Handled (RH, up to 23 Ci/L)
HLW
TRU/LLW
2018
1970
Spent Nuclear Fuel (SNF)
High Level Waste (HLW)
Transuranic Waste (TRU)
Low Level Waste (LLW)
Disposal options for different waste streams begins to diverge in the 1970s

## Slide 11
….seventeen candidate sites for two high-level and commercial waste sites selected in 1982 after the NWPAct
Sites considered for  a second repository
 Sites considered for the first repository

## Slide 12: In 1987, Speaker of the House was Jim Wright from Texas, House majority lead was Tom Foley from Washington State. A junior, Harry Reid, was from Nevada. So Nevada was chosen. Harry Reid became Senate Majority Leader and led the effort to shut down the Yucca Mountain project. In 2008, the YM license application submitted. In 2009, YMP was halted and President Obama put a Blue Ribbon Commission together to develop a new strategy.
In 1987, Speaker of the House was Jim Wright from Texas, House majority lead was Tom Foley from Washington State. A junior, Harry Reid, was from Nevada. So Nevada was chosen.
….powerful eastern politicians removed all eastern sites, removed the second site completely, and by 1987 the remaining western sites were narrowed to three
- Yucca Mt, Nevada
- Hanford, Washington State
- Deaf Smith, Texas

## Slide 13
a simple hydrogeology,
a simple geologic history,
a tectonically interpretable area,
isolation robustly assured for all
types of wastes (no vitrification
or reforming necessary),
minimal reliance on engineered
barriers to avoid long time
extrapolation of models for certain
types of performance,
performance that is independent of the canister, i.e., canister and container requirements are only for transportation, handling and the first several hundred years of peak temperature after emplacement in a repository, and
a geographic region that has an existing and sufficient sociopolitical and economic infrastructure that can carry out operations without proximity to a potentially rapidly growing metropolis (unlikely to ever have human habitation anywhere near the site).
a simple hydrogeology,
a simple geologic history,
a tectonically interpretable area,
isolation robustly assured for all
types of wastes (no vitrification
or reforming necessary),
minimal reliance on engineered
barriers to avoid long time
extrapolation of models for certain
types of performance,
performance that is independent of the canister, i.e., canister and container requirements are only for transportation, handling and the first several hundred years of peak temperature after emplacement in a repository, and
a geographic region that has an existing and sufficient sociopolitical and economic infrastructure that can carry out operations without proximity to a potentially rapidly growing metropolis (unlikely to ever have human habitation anywhere near the site).
a simple hydrogeology,
a simple geologic history,
a tectonically interpretable area,
isolation robustly assured for all
types of wastes (no vitrification
or reforming necessary),
minimal reliance on engineered
barriers to avoid long time
extrapolation of models for certain
types of performance,
performance that is independent of the canister, i.e., canister and container requirements are only for transportation, handling and the first several hundred years of peak temperature after emplacement in a repository, and
a geographic region that has an existing and sufficient sociopolitical and economic infrastructure that can carry out operations without proximity to a potentially rapidly growing metropolis (unlikely to ever have human habitation anywhere near the site).
a simple hydrogeology,
a simple geologic history,
a tectonically interpretable area,
isolation robustly assured for all
types of wastes (no vitrification
or reforming necessary),
minimal reliance on engineered
barriers to avoid long time
extrapolation of models for certain
types of performance,
performance that is independent of the canister, i.e., canister and container requirements are only for transportation, handling and the first several hundred years of peak temperature after emplacement in a repository, and
a geographic region that has an existing and sufficient sociopolitical and economic infrastructure that can carry out operations without proximity to a potentially rapidly growing metropolis (unlikely to ever have human habitation anywhere near the site).
a simple hydrogeology,
a simple geologic history,
a tectonically interpretable area,
isolation robustly assured for all
types of wastes (no vitrification
or reforming necessary),
minimal reliance on engineered
barriers to avoid long time
extrapolation of models for certain
types of performance,
performance that is independent of the canister, i.e., canister and container requirements are only for transportation, handling and the first several hundred years of peak temperature after emplacement in a repository, and
a geographic region that has an existing and sufficient sociopolitical and economic infrastructure that can carry out operations without proximity to a potentially rapidly growing metropolis (unlikely to ever have human habitation anywhere near the site).
a simple hydrogeology,
a simple geologic history,
a tectonically interpretable area,
isolation robustly assured for all
types of wastes (no vitrification
or reforming necessary),
minimal reliance on engineered
barriers to avoid long time
extrapolation of models for certain
types of performance,
performance that is independent of the canister, i.e., canister and container requirements are only for transportation, handling and the first several hundred years of peak temperature after emplacement in a repository, and
a geographic region that has an existing and sufficient sociopolitical and economic infrastructure that can carry out operations without proximity to a potentially rapidly growing metropolis (unlikely to ever have human habitation anywhere near the site).
a simple hydrogeology,
a simple geologic history,
a tectonically interpretable area,
isolation robustly assured for all
types of wastes (no vitrification
or reforming necessary),
minimal reliance on engineered
barriers to avoid long time
extrapolation of models for certain
types of performance,
performance that is independent of the canister, i.e., canister and container requirements are only for transportation, handling and the first several hundred years of peak temperature after emplacement in a repository, and
a geographic region that has an existing and sufficient sociopolitical and economic infrastructure that can carry out operations without proximity to a potentially rapidly growing metropolis (unlikely to ever have human habitation anywhere near the site).
a simple hydrogeology,
a simple geologic history,
a tectonically interpretable area,
isolation robustly assured for all
types of wastes (no vitrification
or reforming necessary),
minimal reliance on engineered
barriers to avoid long time
extrapolation of models for certain
types of performance,
performance that is independent of the canister, i.e., canister and container requirements are only for transportation, handling and the first several hundred years of peak temperature after emplacement in a repository, and
a geographic region that has an existing and sufficient sociopolitical and economic infrastructure that can carry out operations without proximity to a potentially rapidly growing metropolis (unlikely to ever have human habitation anywhere near the site).
Yucca Mt.
As a result, to fully implement the Yucca Mt repository will cost well over $300 billion.
To put the repository in the correct rock would cost only about $30 billion
Yucca Mt. is a highly fractured, oxidizing, variably saturated, dual porosity, hydrologic system that sits on the edge of the Las Vegas Shear Zone
What Makes A Good Deep Geologic Nuclear Waste Repository?
There are seven criteria used to evaluate the suitability of a site for a deep geological repository

## Slide 14
reducing inverts
shotcrete
ceramic coating
titanium drip shield
vitrified waste
package supports
gravel backfill
Extreme re-engineering required to counter-act the choice of the wrong rock
But there is a site that meets all seven criteria and that has already demonstrated it can handle all of our nuclear waste of any type, including high-level waste

## Slide 15
Unknown to most, transuranic waste (bomb waste) continued on into the salt as planned, leading to the Waste Isolation Pilot Plant.
WIPP has shown that geologic disposal of nuclear waste is safe and cost-effective
Only defense-generated TRU waste
presently permitted: 100 nCi/g to 23 Ci/L
of alpha-emitting 239Pu equivalents
but WIPP was originally designed
to handle all nuclear waste
16 miles2 set aside in the 1992 Land Withdrawal Act
- when WIPP is full, only 1/2 mile2 will have been used
Unknown to most, transuranic waste (bomb waste) continued on into the salt as planned, leading to the Waste Isolation Pilot Plant.
WIPP is ahead of schedule and under-budget
Notes: Third there’s WIPP - the Waste Isolation Pilot Plant in southeastern New Mexico.

## Slide 16
Waste Isolation Pilot Plant
U.S. Department of Energy
2,130 feet below the surface
Ventilation system:
425,000 ft3/minute
Constantly monitored
HEPA filtered

## Slide 17
WIPP Salado Formation salt was deposited by repeated evaporation of shallow marine incursions into the Permian Basin of New Mexico
200 nm
1 cm
Length: 4136 nm = ~12, 100 base pairs (similar to modern halophilic bacterial DNA)

## Slide 18
Mining the Salado is the easiest and safest mining operation in the world

## Slide 19
January 2007, high activity waste began shipping to WIPP; up to 1000 R/hr surface and 23 Curies/liter (87 Curies/gallon)

## Slide 20
At the 2000 lbs/inch2 pressure at this depth, the salt exhibits significant creep closure, i.e., the salt completely closes all fractures and openings, even micropores, making the salt extremely tight, such that water cannot move even an inch in a billion years
15 years of operation – 100,000 cubic meters of TRU waste disposed
500,000 fifty-five gallon drum equivalents
21 storage sites cleaned of legacy waste
1 minor release to the environment
0 deaths 0 people contaminated

## Slide 21
Evolution of the WIPP Disposal Rooms (t = 0 yrs)
Courtesy of Frank Hansen, SNL

## Slide 22
Evolution of the WIPP Disposal Rooms (10-15 yrs)
Courtesy of Frank Hansen, SNL

## Slide 23
Evolution of the WIPP Disposal Rooms (1000 yrs)
(water and contaminants move less than an inch in a billion years)
no engineered barriers needed, waste form irrelevant
no persistence of cladding or canister needed
no adverse temperature effects, fluid inclusion migration irrelevant
K ≤ 10-14 m/s
D ~ 10-15 m2/s
performance period - 200,000,000 years, not 10,000 or 100,000 years
1% - 1.5% porosity pH = 8.6 - 9.2 Eh < -500 mV
Ksalt ~ 15 kcal/m/hr/deg @ 200°C = 5 x Kcrystalline
annealing of disturbed salt ~ ƒ(Tx) where 6 < x < 9  closes in < 3 years for HLW

## Slide 24
Waste Disposal Footprint in Salt
Final footprint of WIPP will be only 1 mile2 out of 16 set aside for nuclear waste disposal by the the 1992 Land Withdrawal Act.
Small leak in 2014 does not change anything, WIPP is still 10 yrs ahead of schedule and $1 billion under budget.

## Slide 25
What is in the tanks at the Hanford Nuclear Reservation Washington State?
Waste Tanks

## Slide 26
URANIUM
DISSOLUTION
URANIUM
SEPARATION
COATING REMOVAL WASTE
Other SSTs
SSTs B-201 through B-204,
T-201 through T-204,
and T-104, T-110, & T-111
REPROCESSING
BUILDING 224 CONCENTRATION WASTES
PLUTONIUM DECONTAMINATION
1ST DECON
CYCLE
2ND DECON
CYCLE
IN 224 B & T
PROCESSING PLANTS
PLUTONIUM
CONCENTRATION
PLUTONIUM PRODUCT
METAL WASTE
HLW
TRU
DECONTAMINATION CYCLE
WASTES
FUEL
ASSEMBLIES
CLADDING REMOVAL
(Coating Dissolution)
What is HLW or nuclear bomb waste?
- 57 million gallons at Hanford
- 1.4 million is CH-TRU
IRRADIATED FUEL

## Slide 27
4 mrem/yr

## Slide 28
TIMEFRAME
EPA 40 CFR 191
1,000-year requirement
  4 mrem/year whole body (water)
  25 mrem/year whole body (all pathways)
  75 mrem/year critical organ
10,000-year requirement
  Curie release limits
    1-in-10 chance of exceeding the limit
    1-in-1000 chance of exceeding 10x the limit

## Slide 29
Tank Closure Alternatives For The DOE Environmental Impact Statement

## Slide 30: EIS results for Hanford tank waste – No Action (1) or vitrification with various closure scenarios. Note column showing peak dose at river’s edge ( ) at peak year (e.g., 4978)
Table S-10. tank Closure Alternatives - Summary of Radiation Dose and Hazard Index at
Year of Peak Dose/Hazard Index for the Drinking-Water Well User
Note: Calendar year of peak impact shown in parentheses
Tank Closure Alternative | Core Zone Boundary |  | Columbia River Nearshore | 
 | Radiation Dose (millirem per year) | Hazard Index | Radiation Dose (millirem per year) | Hazard Index
1 (No Action) | 58.88 (4313) | 9.20 (2500) | 4.37 (4978) | 1.01 (4498)
2A | 8.64 (2069) | 5.26 (2068) | 0.941 (2317) | 1.01 (2079)
4\2B, 3A, 3B, 3C, 6C | 7.58 (2056) | 4.81 (2050) | 0.885 (2242) | 0.971 (2076)
4 | 7.41 (2056) | 4.80 (2050) | 0.882 (2242) | 0.971 (2076)
5 | 7.57 (2056) | 4.81 (2050) | 0.894 (4809) | 0.971 (2076)
6A, Base Case | 7.37 (2056) | 4.80 (2050) | 0.876 (2251) | 0.971 (2076)
6A, Option Case | 7.64 (2066) | 5.22 (2051) | 0.899 (2251) | 0.912 (2076)
6B, Base Case | 7.35 (2056) | 4.80 (2050) | 0.822 (2218) | 0.972 (2076)
6B, Option Case | 7.92 (2065) | 5.23 (2083) | 0.807 (2218) | 0.830 (2074)

## Slide 31
About 70 mrem/yr
Medical procedures 53 mrem
Consumer products 10 mrem
One coast to coast airplane flight 2 mrem
Watching color TV 1 mrem
Sleeping with another person 1 mrem
Weapons test fallout less that 1 mrem
Nuclear industry less than 1 mrem
Normal annual exposure from man-made radiation
Normal annual exposure from natural radiation
About 300 mrem/yr
Radon gas 200 mrem
Human body 40 mrem
Rocks, soil 28 mrem
Cosmic rays 27 mrem
  Comparison of 4 mrem/yr Worst-Case Peak Dose from Hanford tanks with Normal Background Radiation
Move to Spokane
50 mrem/yr
Notes: This slide demonstrates that we all receive a total of about 370 mrem (0.37 mSv) of radiation exposure each year from background sources. The range of exposures from background is very high in different environments. Background radiation increases as a function of elevation, as a function of radon in homes and from natural radioactive materials in the environments. There are some areas where the natural background radiation dose is increased by more than a factor of ten. Many of the man made exposure are being regulated at levels much below background. For example there are some very vigorous discussions on whether the level for exposure from man-made sources should be 15 or 25 mrem per year. Since both of these levels are far below the background level, and the range of background level is so high, it is difficult to justify the needed expense required to comply with the lower standard.

## Slide 32: Even though TRU and HLW have different disposal pathways, reclassifying this HLW as TRU or LLW and disposing elsewhere (2R), e.g., WIPP, is identical to vitrification (2A, 3, 4, 5, 6)
Table S-10. tank ClosureAlternatives- Summary of Radiation Dose and Hazard Index at
Year of Peak Dose/Hazard Index for the Drinking-Water Well User
Note: Calendar year of peak impact shown in parentheses
Tank Closure Alternative | Core Zone Boundary |  | Columbia River Nearshore | 
 | Radiation Dose (millirem per year) | Hazard Index | Radiation Dose (millirem per year) | Hazard Index
1 (No Action) | 58.88 (4313) | 9.20 (2500) | 4.37 (4978) | 1.01 (4498)
2R (non-DOE estimate) | 8.10 (2400) | 5.10 (2300) | 0.910 (2700) | 0.990 (2080)
2A | 8.64 (2069) | 5.26 (2068) | 0.941 (2317) | 1.01 (2079)
4\2B, 3A, 3B, 3C, 6C | 7.58 (2056) | 4.81 (2050) | 0.885 (2242) | 0.971 (2076)
4 | 7.41 (2056) | 4.80 (2050) | 0.882 (2242) | 0.971 (2076)
5 | 7.57 (2056) | 4.81 (2050) | 0.894 (4809) | 0.971 (2076)
6A, Base Case | 7.37 (2056) | 4.80 (2050) | 0.876 (2251) | 0.971 (2076)
6A, Option Case | 7.64 (2066) | 5.22 (2051) | 0.899 (2251) | 0.912 (2076)
6B, Base Case | 7.35 (2056) | 4.80 (2050) | 0.822 (2218) | 0.972 (2076)
6B, Option Case | 7.92 (2065) | 5.23 (2083) | 0.807 (2218) | 0.830 (2074)

## Slide 33
33 USCS § 1402 (j) and 10 CFR 60.2 (1) define high-level radioactive waste as liquid wastes resulting from the operation of the first cycle solvent extraction system, and the concentrated wastes from subsequent extraction cycles, in a facility for reprocessing irradiated reactor fuel, and any solids into which such liquid wastes have been converted.
What Would We Do To Reclassify This Waste to What It Really Is?
What is defense high-level nuclear waste?

## Slide 34
URANIUM
DISSOLUTION
URANIUM
SEPARATION
COATING REMOVAL WASTE
Other SSTs
SSTs B-201 through B-204,
T-201 through T-204,
and T-104, T-110, & T-111
REPROCESSING
BUILDING 224 CONCENTRATION WASTES
PLUTONIUM DECONTAMINATION
1ST DECON
CYCLE
2ND DECON
CYCLE
IN 224 B & T
PROCESSING PLANTS
PLUTONIUM
CONCENTRATION
PLUTONIUM PRODUCT
METAL WASTE
HLW
TRU
DECONTAMINATION CYCLE
WASTES
FUEL
ASSEMBLIES
CLADDING REMOVAL
(Coating Dissolution)
What is HLW or nuclear bomb waste?
- 57 million gallons at Hanford
- 1.4 million is CH-TRU
IRRADIATED FUEL

## Slide 35: the nature of defense high-level nuclear waste
HLW must be:
highly radioactive,
result from reprocessing spent nuclear fuel for weapons, and
if a solid waste that was derived from liquid waste produced directly in reprocessing, it must contain fission products in sufficient concentrations to require permanent isolation.
neutron
90Sr
137Cs
0
.
0
0
0
1
0
.
0
0
1
0
.
0
1
0
.
1
1
1
0
5
0
7
0
9
0
1
1
0
1
3
0
1
5
0
1
7
0
% yield
mass number
90Sr
137Cs

## Slide 36: the nature of defense high-level nuclear waste
HLW must be:
highly radioactive,
result from reprocessing spent nuclear fuel for weapons, and
if a solid waste that was derived from liquid waste produced directly in reprocessing, it must contain fission products in sufficient concentrations to require permanent isolation.
The House Armed Services Committee provided a rationale for changing the HLW definition from the prior source-based definition to a source plus hazard-based definition - it should matter what’s in the waste.
Congress provided better language to DOE when it defined high-level radioactive waste (HLW) in the Nuclear Waste Policy Act of 1982 (NWPA) directing government agencies to consider both the source and the hazard of wastes before classifying the waste as HLW or otherwise.
Unfortunately, at the time NRC refused to define the word sufficient, believing that “the principles of waste classification were well known”

## Slide 37
To find a conservative interpretation of sufficient, the best and only reasonable place is:
10 CFR 61.55 defines these sufficient limits as 7 Ci/liter for 90Sr and 4.6 Ci/liter for 137Cs, below which radioactive waste can go into a shallow landfill.
the nature of defense high-level nuclear waste
99% of Hanford HLW tanks have less than 1 Ci/liter of either 90Sr or 137Cs
  most Cs/Sr removed for use in research and to control heat in the tanks, and the rest has gone through 1 or 2 decay lives
  some of the waste has alpha-emitting radionuclides exceeding 100 nanoCi/g of 239Pu equivalent (lower limit for TRU in WIPP) and all have radioactivity less than 23 Ci/liter (upper limit for TRU in WIPP)
Therefore, 56 million out of 57 million gallons of Hanford HLW tank waste is no longer HLW except in name, but does meet the material definition of TRU or LLW
Is it possible to incorporate this observation into our long-term disposal program?
Do we care what’s real?

## Slide 38: What would an alternative plan look like for Hanford Tank waste?
Scenarios – 1) vitrify all 2) vitrify a little (600k gallons) 3) vit none
Waste Sludge (11 million gallons)
  1.4 million gallons is contact-handled transuranic waste (CH) that could be retrieved, dried, packaged, and disposed of at WIPP following a Class 3 Permit Modification approved by the State of New Mexico -- much of this is in the leaking tanks
  9.6 million, presently intended for pretreatment in the WTP, could be dried and packaged for about a fourth of the cost of the WTP, resulting in about 3.5 million gallons of packaged waste acceptable to WIPP in < 20 years.
  Rail transport using dedicated containers and trains - rail spurs already in place at Hanford and WIPP
  < $10 billion total
Saltcake and Supernatant Waste (45 million gallons)
  supernatant, mixed with water, used to dissolve tank saltcake wastes
  could be immobilized as LAW for disposal at Hanford or Texas using a combination of drying and cast-stoning for about $12 billion
Or liquid could be dried down to about 35 million gallons of solid, and disposed in WIPP, taking an additional 15 years for WIPP, totaling < $8 billion

## Slide 39: What would an alternative plan look like for Hanford HLW?
Baseline (as HLW) > $400 billion, > 60 years
Alternative (as TRU/LLW) < $50 billion, < 30 years
This alternative is likely the only path to satisfy the anticipated cost and schedule deadlines of the Tri-Party Agreement
Recently, the estimated cost of the present vitrification program has risen to $400 billion and > 60 years

## Slide 40: Required Changes to the WIPP Land Withdrawal Act (LWA P.L. 102-579)
LWA provides EPA regulatory authority through 40 CFR Part 191
LWA limits the total capacity of TRU waste to 6.2 million ft3 (175,570 m3)
LWA limits the total radioactivity of RH waste to 5.1 million curies
Consultation and Cooperative Agreement with the State of New Mexico (1981)
  total Remote Handled (RH) TRU capacity of 250,000 ft3 (7,080 m3)
  total Contact Handled (CH) TRU capacity of 5.95 million ft3 (168,490 m3)
Regulatory changes needed for NM (NM is an Agreement State)
Repeal 2004 Category 3 Permit Mod prohibiting tank waste of any sort
Increase above limits to handle increased defense waste volumes
Modify LWA to acceptance of non-TRU waste or re-categorize defense HLW waste as TRU
Modify RCRA permit with the New Mexico Environment Department
Modify Compliance Certification with the EPA
Changes to the Low-Level Radioactive Waste Policy Amendment Act (LLRWPAA) to authorize EPA to regulate other waste at WIPP
  DOE Order 435.1, NWPA 1982, Tri-Party Agreement, NEPA, etc.
WDoE would rather change LWA; NM would rather designate HLW as TRU

## Slide 41
Waste Disposal Footprint in Salt
New footprint of an expanded WIPP to include HLW that has become RH-TRU, with interim storage for SNF, would be less than 3 mile2 out of the 16 set aside for nuclear waste disposal by the the 1992 Land Withdrawal Act

## Slide 42
- least tectonically deformed, thickest, most optimal depths
WCS
Andrews
TX
•

## Slide 43
Interim Storage for Commercial Spent Fuel
-ideal for hundreds of years, enough time for SNF to no longer be high-activity

## Slide 44
Deep Borehole Injection of Nuclear Waste

## Slide 45
Probable Outcomes for U.S. Nuclear Waste (also supported by BRC)
Defense Waste (TRU and
HLW)
Commercial nuclear fuel
•
HLW redefined as TRU
stays right where it is
(EISs show no problem)
WIPP
Second salt repository
Burn in fast reactors later this century
Deep borehole
2nd salt repository - cheap
Interim storage

## Slide 46
Thank You!
Questions?

## Slide 47
15 years of operation – 100,000 cubic meters of TRU waste disposed
500,000 fifty-five gallon drum equivalents
21 storage sites cleaned of legacy waste
1 minor release to the environment
0 deaths 0 people contaminated
On Valentine’s Day 2014, a puff of airborne radioactivity was detected in the WIPP underground. Immediately, ventilation went to HEPA. The amount released was 1.8 Bq/m3 of air (not even reportable as per EPA) that quickly dropped to hundredths of a
Bq/m3, measureable but a thousand times less than background doses. 21 Workers had detectable amounts that quickly disappeared, also well below human background.

## Slide 48
Waste Isolation Pilot Plant
U.S. Department of Energy
2,130 feet below the surface
Ventilation system:
425,000 ft3/minute
Constantly monitored
HEPA filtered
Truck Fire 2/5/14
Drum Breach
2/14/14

## Slide 49
On Valentine’s Day 2014, a puff of airborne radioactivity was detected in the WIPP underground. Immediately, ventilation went to HEPA. The amount released was 1.8 Bq/m3 of air (not even reportable as per EPA) that quickly dropped to hundredths of a
Bq/m3, measureable but a thousand times less than background doses. 21 Workers had detectable amounts that quickly disappeared, also well below human background.

## Slide 50: 1970s-80s - metal-nitrate salts in nitric acid generated from experiments to remove Am from older weapons 1970s - experiments to remove Am from weapons materials; generated metal-nitrate salt waste 2011 - retrieved for packaging for WIPP, procedures altered to remove warnings about metal nitrates absorbents and neutralizer addition, some incompatible with waste, Pb 2013 - advised to add inorganic cat litter, someone switched to organic dustless litter, and shipped to WIPP 2014 - drum heats up, pops top, releases rad, WIPP closed May 19 NMED issues two Admin Orders - corral drums not in WIPP, make secure - seal WIPP Panel 6 and Panel 7 room 7
Clean-up could have taken 6 months and $50 million
DOE took 3 years and $500 million to clean-up
Lots of studies, redo all procedures, start from ground up, correct all issues which were mostly bureaucratic. New Ventilation, new shafts. But this leak was not a problem with the WIPP repository itself.
The nitrate waste drums

## Slide 51
Neutralizers and sorbents included sodium carbonate, triethanolamine and polyacrylate. Anhydrous citric acid (a reducer) was used adjust pH. A strong acid should never be added to a strong oxidizer
– this is a Chem 101 no-no
And citric acid should never be used with metal-nitrate salts, because of the rapid evolution of heat. Similarly for acrylates.

## Slide 53
The Pre- and Post-radiological event 239+240Pu concentrations in ambient air at three stations in the vicinity of WIPP (Post-release dates from July 2014 to December 2016)